## Slide 1
Tracking Wrist Motion to Monitor Energy Intake
Adam Hoover
Electrical & Computer Engineering Department

## Slide 2: Current Tools
Manual counting
Calorie or food diary
Problem #1: Not easy to use for long period of time
Problem #2: Underestimation/underreporting bias
24-hour recall (interview)

## Slide 3: Wrist Roll Motion
Wrist rolls to get food from table to mouth
Roll is independent of other axes of motion

## Slide 4
Demo of Bite Counting
Early test: 49 meals (47 participants), 1675 bites
86% bites detected, 81% positive predictive value
Talking and other actions between 67% of bites

## Slide 5: Harcombe Cafeteria
Main food service for Clemson University
Seats ~800 people
Huge variety of foods and beverages

## Slide 6: Cafeteria Experiment
276 participants (1 meal each)
380 different foods and beverages consumed
22,383 total bites
82% bites detected, 82% positive predictive value

## Slide 7: Bite Counting Accuracy
Accuracy increases with age (77% 18-30, 88% 50+)
Minor variations in accuracy due to utensil, container, gender, ethnicity
most accurate food:
salad bar (88%)
least accurate food:
ice cream cone (39%)
Currently studying this “Bite Database”

## Slide 8
Lab model
Watch model
Embedded System Design
Stores time-stamped log of meals (bite count)
Audible alarm
On/off button

## Slide 9: Bite-to-Calorie Correlation
each point = 1 meal
2 weeks data (~50 meals), 1 person

## Slide 10: Correlation Test
0.4 correlation
0.7 correlation
83 subjects wore for 2 weeks, 3246 total meals
each plot = 1 person

## Slide 11: Correlation Comparison
Physical activity monitors 1
Energy expenditure
Our device
Energy intake
76% ≥ 0.4
1 Westerterp & Plasqui, 2007, "Physical Activity Assessment with Accelerometers: An Evaluation against Doubly Labeled Water", in Obesity, vol 15, pp 2371-2379.

## Slide 12: Converting Bites to Calories
kpb (male) = 0.2455 h + 0.0449 w − 0.2478 a
kpb (female) = 0.1342 h + 0.0290 w − 0.0534 a
kpb = kilocalories per bite
Formula based on height (h), weight (w), age (a)
Formula fit using 83-people 2-week data set
Tested on 276 meals cafeteria data set

## Slide 13: Calories in Cafeteria Meals

## Slide 14: Error: Mean and Variance

## Slide 15: Applications
  Weight loss/maintenance
  Objective, automated monitoring
  Cognitive workload
  Offload energy intake monitoring
  Real-time feedback
  The device can give cues to stop eating

## Slide 16: Observation Applications
time
of
day
#bites

## Slide 17: Questions?
For more info: www.ces.clemson.edu/~ahoover