## Slide 1
Adam Hoover
Industrial Computer Vision Inspection Systems

## Slide 2
Adam Hoover, JP Kwon, Raul Ramos,
Ryan Mattfeld
Joerg Schulte, Brenden MacAskill,
Katie Jurewicz
Automatic Visual Inspector

## Slide 3: BMW Spartanburg
Opened in 1994, 1,150 acre facility
$12 billion cost to build (more since then)
~11,000 employees
500,000 vehicles per year

## Slide 4: Cars are Custom
Thousands of custom part options
Sun roof
Engine
Tires
Proximity sensors
Roof rack
Entertainment
Seats

## Slide 5: BMW Assembly Line - Robots
Reliable for repeated operations

## Slide 6: BMW Assembly Line - Humans
Better at flexible assembly

## Slide 7
Check tool kit installation
Check badge installation
Badge identifies engine model
Wrong badge installed ~1-2% of cars
Car inspection: example problems
Problems manually inspected by human
Human catches ~80% errors
Lots of similar problems
Hex attachment included in some cars
Depends on tire selected

## Slide 8: Goal: Assist Human Inspector
workflow
cameras
01023
01017
workflow
Site: Hall 50,
door assembly
Result indicator
Goal: Human inspector is still in charge of final result; machine inspector saves time by prompting only when problem spotted
IPS -> car information (options)
Door assembly work

## Slide 9: System Setup

## Slide 10: Setup Program
Replay video, pause at examples of inspection problem, draw rectangles.

## Slide 11
Why two search areas?
Inspection = thing to be inspected. Can vary.
Trigger = nearby part that can be expected to always be there. Does not vary.

## Slide 12
Why two rectangles?
Search window allows for variability in positioning.
Template is appearance of thing to be inspected.

## Slide 13
Image processing core
Normalized cross correlation
Template
Search area
Matching score (brighter = higher)
Highest match

## Slide 14
More examples

## Slide 15
Inspecting shock absorbers
Inspecting bolts on underbody
Occlusion of camera or lighting (shadows) can hinder inspection process
Image Processing Challenges - Occlusion

## Slide 16
Image Processing Challenges - Occlusion
No occlusion
Intermittent occlusion
Comparison of class matching over time
Variance of class matching is a strong indicator of occlusion
Algorithm developed to use this concept to detect occlusions

## Slide 17
“detectability” (single bright dot = good)
The engineer installing our system for a new problem has no computer vision expertise. We built this interface to help them visualize the quality of their setup (training data).
Setup Challenges for New Problems

## Slide 18
Child safety lock inspection

## Slide 19
This template is too small and matches many areas across the whole search window.
This template is better, but still shows the difficulty of this inspection problem. The shape best matches in the center but partially matches in other places.
Bad detectability
Better detectability
Detectability vs Window Size

## Slide 20
Templates of child safety lock not present
Templates of child safety lock present
While training VI, templates are provided of each class (e.g. present versus absent). The templates should cover the variability expected (e.g. shape, placement, color).
Training Data Quantity vs Class Similarity

## Slide 21
Source: child safety lock, present vs absent
CC = cross correlation, defines how well each template matches within its class versus other classes
Some inadvertent training data led to diminished accuracy.
Cross-comparing all training data

## Slide 22
Adam Hoover
Surya Sharma
Ben Shumpert
Zeyu Tang
Factory in Newberry, SC, USA
Appliance Inspection System
Anatole Figueroa
Simon Brown
Vihang Khare

## Slide 23
Camera locations

## Slide 24
Inspection with varying appearance

## Slide 25
Red water valve connector
Five examples: variability in position, orientation, and occlusion
Variability when not properly installed

## Slide 26
EMI Filter
Wire Holder
Red Water Valve
White Water Valve
Hose Clamp
Pressure Sensor
Inspection Problems

## Slide 27
Inspection Problems

## Slide 28
Results
Inspection problem | Images | Defects (manual review) | Defect rate | Percent of defects detected | False alarms per defect
EMI filter | 39,268 | 31 | 0.08% | 97% | 4
Red water valve | 38,447 | 89 | 0.23% | 98% | 1.8
White water valve | 32,250 | 83 | 0.26% | 100% | 0.1
Hose clamp | 39.268 | 31 | 0.07% | 100% | 2.5
Wire holder | 36,658 | 180 | 0.49% | 35% | 5
Pressure sensor | 13,009 | 2 | 0.02% | 100% | 0
Thermistor | 23,247 | 12 | 0.05% | 92% | 2
Screw near thermistor | 23,245 | 23 | 0.10% | 100% | 0.6
Defect types
Note this is after human inspections
Our system performance on what the humans missed
Part absent
Wrong part installed
Part not tightened
Trigger failure (washing machine not in camera’s field-of-view)
Occlusion (part completely obscured)

## Slide 29
Drum ring
Installed correctly
Missing

## Slide 30
Q-eye inspecting top left

## Slide 31
Q-eye inspecting top right

## Slide 32
Results
Inspection problem | Images | Defects (manual review) | Defect rate | Percent of defects detected | False alarms per defect
Drum ring* | 32,903 | 18,387 | 55.9% | 96% | 0.3
Upper screw assembly | 15,942 | 124 | 0.78% | 100% | 1.2
Screw 3 | 15,942 | 130 | 0.82% | 98% | 4.2
Screw 4 | 15,942 | 54 | 0.34% | 100% | 3.4
Screw 5 | 15,942 | 236 | 1.48% | 97% | 4.4
Screw 6 | 15,942 | 225 | 1.41% | 100% | 4
Screw 7 | 15,942 | 225 | 1.41% | 100% | 0.6
Defect types
Our system performance
Part absent
Part not tightened
Extra drum ring installed (double)
Trigger failure (part not in camera’s field-of-view)
*Drum ring: an associate was assigned to add the drum ring after the camera location during our data collection, which caused a large number of detects to be observed

## Slide 33
NEXIS vs Q-Eye
Our NEXIS inspection system had similar success in finding defects to their Q-Eye systems, but with up to 10x less false positives.
Note: these inspection problems are MUCH easier than the variable appearance problems, which Q-Eye could not handle at all.

## Slide 34
Computer Vision Across Industries
Package Routing
Chip Inspection