## Slide 1
Inertial Measurement Unit
Adam Hoover

## Slide 2
Outline
Accelerometer
Gyroscope
Magnetometer
Inertial measurement unit (IMU)
Applications
IMU in Apollo spacecraft (circa 1965)
IMU in chip ($7 circa 2020)

## Slide 3
Accelerometer Physics
F = kx
m
x
0
(rest)
F = force applied, k = spring constant, x = distance moved
F = ma
F = force applied, m = mass, a = acceleration
a = kx/m
solve for acceleration based on distance moved

## Slide 4
MEMS Accelerometer
[reference]
x0
x1
CA
CB
distance capacitors move related to capacitance change
manufactured along multiple axes to measure accelerations in x, y, z directions
MEMS = microelectromechanical system

## Slide 5
Accelerometer Data
[reference]
velocity = integral (acceleration)
distance = integral (velocity)
units = m/s2 or G
units = m/s
units = m

## Slide 6
Integration Error
[reference]
error due to sampling
errors are magnified during integration, even worse during double integration
error can be reduced by linear interpolation or curve fitting

## Slide 7
Accelerometer On Earth
[reference]
Earth exerts 1G force independent of object motion
as sensor rotates, Earth’s vector changes making it difficult to “subtract out”
human motions can have very small accelerations compared to Earth’s gravity
G
0
1
x
y
z
time
object at rest will show effect of Earth’s gravity

## Slide 8
Linear Motion
Can accelerometers (or inertial measurement units) reliably track linear motion?
No

## Slide 9
Gyroscope Physics
gyroscopes measure radial velocity
spinning two axes causes a radial force on the third axis
gaining momentum
losing momentum
losing momentum
gaining momentum
An orthogonal force (arrows) results from the material gaining and losing momentum due to the two rotations
[reference]
[demo]

## Slide 10
MEMS Gyroscope
[reference]
Vibrations are driven in one direction using oscillator.
As rotation happens in second direction it can be measured in third direction using capacitors.
manufactured along multiple axes to measure rotations around x, y, z axes

## Slide 11
Gyroscope Data
single integration yields radial position
raw gyro data
units = rad/s or deg/sec
units = rad or deg
first measurement?
radial position is relative to first measurement
degrees rotated
meas
absolute orientation unknown
drift due to integration
much less than accelerometer

## Slide 12
Magnetometer Physics
magnetometer measures strength of magnetic field
it is assumed that Earth is providing the dominant magnetism to the sensor
[reference]
using a 3-axis magnetometer, direction = arctan(My / Mx)
sensor units are T (micro Tesla)

## Slide 13
Magnetometer Errors
problem | source
local magnetic fields | electronics, speakers
magnetic declination | tilt between celestial and magnetic poles
magnetic dip | variation in “down” from equator to poles
geographical variation | Earth’s geology
global coordinate system, but very noisy

## Slide 14
IMU
IMU = accelerometer + gyroscope + magnetometer
combines strengths of each to help overcome weaknesses of each
MEMS IMU includes processor to perform computations that combine individual sensor measurements
various algorithms used to filter noise and combine measurements to achieve absolute (coordinate system) position and orientation tracking

## Slide 15
IMU Applications
applications where tracking with cameras is impractical and tracking with GPS is not accurate enough