## Slide 1
Building the Bite Counter
Adam Hoover
Electrical & Computer Engineering Department

## Slide 2: Outline
Motivation, existing tools, related work
Tracking wrist motion to count bites
Relating bites to calories
Design and manufacturing

## Slide 3
Motivation
Prevalence of obesity
  Worldwide: 1.9 billion adults (39%) are overweight and 650 million adults (13%) are obese (WHO 2016). Meter.
  USA: 37.7% of adults are obese and 17.2% of children are obese (Ogden et al. 2016).
Source:
NIDDK, 2018

## Slide 4
Costs
(Mokdad et al, Actual causes of death in the United States, 2004, JAMA)
Comorbidities: Diabetes, heart disease, high blood pressure, stroke, and higher rates of certain cancers (Wellman et al. 2002)
Annual medical cost in the United States: $147 billion in 2008 (Finkelstein et al. 2009)

## Slide 5
Energy Measures
Energy Intake (Calories or Joules) | Energy Expenditure (Calories or Joules)
Energy absorbed through food intake. | Homeostasis (body maintenance), exercise.
<- weight change ->

## Slide 6: Clinical Tools
Calorimetry Chamber
(measures EE)
Bomb Calorimeter
(measures EI if exact same serving fully consumed)
Doubly Labeled Water
(measures EE directly, EI indirectly*)
*Over a week, EI – EE = weight change

## Slide 7: Free-Living Tools: EE
EE: physical activity monitors, pedometers

## Slide 8: Free-Living Tools: EI
EI: food diary, manual counting, database-assisted logs
Problem #2: Underestimation/underreporting bias (dozens of studies have found it ranges 10-50%, evaluated using doubly labeled water)
Challenge: Develop body-worn sensors similar to activity monitors
Problem #1: Compliance (not easy to use for long period of time)

## Slide 9
Wearable sensor-based approaches
  Lanyard camera
  (e.g. Gemming et al. 2013)
  Video record eating activities
  Throat and ear
  (e.g. Sazonov et al. 2010)
Detect swallows, chewing sounds
Free-living challenges: Accuracy, compliance (social stigma, comfort, ruggedness, battery life)
  Glasses
  (e.g. Kleinberg et al. 2015)
Head movements

## Slide 10
Our concept: Bite Counter
Tracks wrist motion to detect eating activities and count bites (hand-to-mouth gestures)
Audible alarms to queue behaviors such as slowing eating or portion control
Worn like a watch

## Slide 11: Outline
Motivation, existing tools, related work
Tracking wrist motion to count bites
Relating bites to calories
Design and manufacturing

## Slide 12: Wrist Roll Motion
Wrist rolls to get food from table to mouth
Roll is independent of other axes of motion

## Slide 13: Algorithm
The wrist undergoes a characteristic roll motion during the taking of a bite of food that can be tracked using a gyroscope
Biologically, this can be related to the necessary orientations for (1) picking food up, and (2) placing food into the mouth

## Slide 14
Demo of Bite Counting
Early test: 49 meals (47 participants), 1675 bites
86% bites detected, 81% positive predictive value
Talking and other actions between 67% of bites
Y. Dong, A. Hoover, J. Scisco and E. Muth, "A New Method for Measuring Meal Intake in Humans via Automated Wrist Motion Tracking", in Applied Psychophysiology and Biofeedback, vol 37, no 3, 2012, pp 205-215.

## Slide 15: Cafeteria Experiment
Main food service for Clemson University
Seats ~800 people
Huge variety of foods and beverages

## Slide 16: Cafeteria Experiment
276 participants (1 meal each)
374 different foods and beverages consumed
24,088 total bites
81% bites detected, 83% positive predictive value
Y. Shen, J. Salley, E. Muth and A. Hoover, "Assessing the Accuracy of a Wrist Motion Tracking Method for Counting Bites across Demographic and Food Variables", in IEEE Journal of Biomedical and Health Informatics, vol. 21 no. 3, March 2017, pp. 599-606.

## Slide 17: Cafeteria Demo

## Slide 18: Bite Counting Accuracy
Accuracy increases as seconds per bite slows
(age, gender, ethnicity)
Accuracy modestly correlates with total wrist motion
(head-toward-plate vs hand-towards-mouth motion)
most accurate food:
salad bar (87%)
least accurate food:
ice cream cone (37%)
Y. Shen, J. Salley, E. Muth and A. Hoover, "Assessing the Accuracy of a Wrist Motion Tracking Method for Counting Bites across Demographic and Food Variables", in IEEE Journal of Biomedical and Health Informatics, vol. 21 no. 3, March 2017, pp. 599-606.

## Slide 19: Outline
Motivation, existing tools, related work
Tracking wrist motion to count bites
Relating bites to calories
Design and manufacturing

## Slide 20
Lab model
Watch model
Embedded System Design
Stores time-stamped log of meals (bite count)
On/off button
Free app

## Slide 21: Bite-to-Calorie Correlation
each point = 1 meal
2 weeks data (~50 meals), 1 person

## Slide 22: Correlation Test
0.4 correlation
0.7 correlation
83 subjects wore for 2 weeks, 3246 total meals
each plot = 1 person
J. Scisco, E. Muth and A. Hoover, "Examining the Utility of a Bite-Count Based Measure of Eating Activity in Free-Living Humans", in Journal of the Academy of Nutrition and Dietetics, vol. 114 no. 3, April 2014, pp. 464-469.

## Slide 23: Correlation Comparison
Physical activity monitors 1
Energy expenditure
Our device
Energy intake
76% ≥ 0.4
1 Westerterp & Plasqui, 2007, "Physical Activity Assessment with Accelerometers: An Evaluation against Doubly Labeled Water", in Obesity, vol 15, pp 2371-2379.

## Slide 24: Converting Bites to Calories
kpb (male) = 0.2455 h + 0.0449 w − 0.2478 a
kpb (female) = 0.1342 h + 0.0290 w − 0.0534 a
kpb = kilocalories per bite
Formula based on height (h), weight (w), age (a)
Formula fit using 83-people 2-week data set
Tested on 276 meals cafeteria data set
J. Salley, A. Hoover, M. Wilson and E. Muth, "A Comparison Between Human and Bite-Based Methods of Estimating Caloric Intake", in Journal of the Academy of Nutrition and Dietetics, vol. 116 no. 10, pp. 1568-1577.

## Slide 25: Calories in Cafeteria Meals

## Slide 26: Outline
Motivation, existing tools, related work
Tracking wrist motion to count bites
Relating bites to calories
Design and manufacturing

## Slide 27
Embedded System Design
Laboratory
experiments
(2007)
1st gen (2011)
($35k + labor)
2nd gen (2015)
($125k + labor)

## Slide 28
Breadboarding and parts selection
gyroscope
LCD
processor
battery, holder
charger
I/O (buttons, speaker, vibratory motor, USB port)

## Slide 29
Processor
development board
dev board JTAG-USB
Texas Instruments MSP430 selection guide

## Slide 30
LCD
surfboard and custom
breakout board
2nd gen custom LCD design
top row 7 seg (values), bottom row 16 seg (units)
pins

## Slide 31
Gyroscope
typically follow “application circuit” from manual
2nd gen includes accelerometer,
used for pedometer function

## Slide 32
Battery
How long will it run?
What can you wear?
1st gen used coin package
2nd gen used square package
(wearables industry)

## Slide 33
Design stages
Breadboard
Circuit diagrams

## Slide 34
Design stages
Circuit diagrams
Printed circuit board (PCB) & manufacturing

## Slide 35
Bite counter PCB
gyroscope
processor
LCD
battery
USB port
USB-RS232 bridge
speaker
buttons
JTAG
charger
1st gen PCB

## Slide 36
Design stages
Industrial designer

## Slide 37
Design stages
PCB design
Molding and case production
Industrial designer

## Slide 38
Design stages
Molds cost $10k (1st gen), $40k (2nd gen)

## Slide 39
Design stages
PCB, case
Assembly

## Slide 40
Design stages
Package design and manufacturing