## Slide 1
Adam Hoover
Introduction to Embedded Computing

## Slide 2
Computing Fundamentals
All these devices include:
Processor(s)
Memory
Bus
Input/output (I/O)
All computations use:
Binary data (1’s and 0’s)
Fetch/Decode/Execute
Instruction Set Architecture (ISA)
How do they differ?

## Slide 3
Design Axes
Suppose you have a travel problem…
Transportation modes differ in:
Size
Cost
Fuel
Origination/Destination
…

## Slide 4
Distance as the design axis
Distance to be travelled
mode

## Slide 5
Computing Design Axes
Differences could include:
Size
Cost
“Processing power”
  Processor clock speed
  Computations/second
  Memory bandwidth
  # processing elements (cores)
“Display power”
  Frame rate
  Triangles/second
  Screen size
These are classic axes for desktops,
laptops, etc.

## Slide 6
Data Type Axis
Data type | Example product
Boolean | 
Numeric | 
Text | 
Transaction | 
Sound | 
Image/video | 
Elevator
Clock, pedometer
Video player,
smartphone
Airport departures,
highway message
boards
ATM (banking),
cash register
Smoke alarm,
surround sound

## Slide 7
Data Type Axis
Data type | Example product | Input | Output | Computing components
Boolean | Elevator |  |  | 
Numeric | Clock, pedometer |  |  | 
Text | Airport departures, highway message boards |  |  | 
Transaction | ATM (banking), cash register |  |  | 
Sound | Smoke alarm, answering machine |  |  | 
Image/video | Video player, smartphone |  |  | 
Push buttons
On/off lights
Switches, dials
Segmented
display
Keyboard
Dot matrix
display
Keypad
Text display
(font)
Microphone
Speakers
Camera
Graphics display
(pixels)
?

## Slide 8
Data Types
Boolean:
0 => false
1 => true
What is 10011?
TFFTT
Unsigned magnitude:
each bit => 2n
1+2+16=19
Signed magnitude:
1st bit => sign
remaining bits => 2n
-3
Two’s complement:
positive integers => unsigned mag
negative integers => reverse bits, add 1
01100+00001 = 01101
-(1+4+8) = -13

## Slide 9
Data Types
Makes addition/subtraction easy.
Positive/negative numbers handled the same.
Example:
5 + (-2) = 3
5 => 00101
+2 => 00010
-2 => 11101 + 00001 => 11110
5 + (-2) => 00101
+ 11110
---------
1 00011 (throw away carry bit) = 3
Why use two’s complement?
circuit in chip
Computing chips customized to work with different data types

## Slide 10
Data Types
Fixed point:
n spans - to + in 2n
decimal point fixed
example: 22 21 20 2-1 2-2
What is 10011?
4.75
Signed fixed point:
as above, 1st bit => sign
-0.75
Floating point:
sign bit
s bits for significand
e bits for exponent
formula varies but basic idea is
number = (sign) 1.s × 2e
-1.00 × 23 = -8.0

## Slide 11
Data Types
ASCII:
7-bit patterns of alphanumeric and control signals
examples:
0100 0001 => 65 => A
0101 1101 => 93 => a
0000 1001 => 9 => horizontal tab
What is 10011?
5/8 of a character?
UNICODE:
32-bit patterns (all language symbols)
example:
0000 0011 1100 0000 => 03C0 (hex) => π
5/32 of a character?

## Slide 12
Data Types
Sound: air pressure measured over time

## Slide 13
Data Types
Digitizing sound
Sampling rate
Bit depth
Design choices include:
Sampling rate
  44 KHz common
Bit depth
  8, 16, 24, 32
Encoding:
  Pulse code modulation (PCM)
  differential PCM
#channels
  1 => mono
  2 => stereo
  6 or 7 => surround

## Slide 14
Data Types
Image: visible light measured over space
similar phenomenon to sound, but
(a) much faster! 390-700 nm waves => 430-790 teraHz
computing circuits cannot sample this fast
instead, accumulate total power during open shutter
(b) many more channels! 480x640, 1024x768, etc.
digitize each channel separately into “pixel”
Design choices include:
Wavelength frequencies (RGB, greyscale, IR)
Raster size
Sampling rate (for video)
Pixel encoding (lots of choices)

## Slide 15
Data Type Axis
Data type | Example product | Input | Output | Computing components
Boolean | Elevator | Push buttons | On/off lights | Different types of processors, memories, buses, data compression, operating systems, and I/O interfacing
Numeric | Clock, pedometer | 0-9 keypad | Segmented display | 
Text | Airport departures, highway message boards | Keyboard | Dot matrix display | 
Transaction | ATM (banking), cash register | Keypad | Text display (font) | 
Sound | Smoke alarm, answering machine | Microphone | Speakers | 
Image/video | Video player, smartphone | Camera | Graphics display (pixels) |