## Slide 1
Chip and Circuit Board Debugging
Adam Hoover
JTAG

## Slide 2
1980’s explosion of embedded computing products
Background

## Slide 3
Mass production of chips … how to test in bulk?
Background
Mass production of products … how to test in bulk?

## Slide 4
Chip fails in a product … how to find which part failed?
Background

## Slide 5
During product development … how to debug/observe code?
Background

## Slide 6
How to see inside a chip?
X-ray
Can see traces, detect breaks How to test functionality?
Used for inspection Non-break failures?

## Slide 7
Oscilloscope
How to see inside a chip?
Pins getting smaller and smaller Lots of pins!
Pins underneath the chips How to affect, record?

## Slide 8
Dedicate some pins to test and debug
Read voltages from other pins or circuitry inside chip via debug pins
When turned on, in debug mode; when turned off, operate normally
Boundary Scanning

## Slide 9
Industry manufacturers were all making custom solutions
JTAG = Joint Test Action Group
IEEE 1149.1 Standard Test Access Port (TAP) and Boundary-Scan Architecture
(mouthful, let’s just call it JTAG)
Background

## Slide 10
JTAG pins
TDI = input TDO = output
TCK = clock TMS = test mode select (turn JTAG on/off)
Input/output voltages
Shifted through latches
on pins around the
boundary of the chip

## Slide 11
Multiple chips
Connect chips in series

## Slide 12
Details
Buffer bits to form JTAG instruction
Execute JTAG instruction
Shift in/out
1 bit at a time
Dual-use some pins for
more debugging options
Some default instructions:
BYPASS (TDO = TDI)
SAMPLE/PRELOAD
IDCODE (chip ID)
INTEST (run internally hold pins)
CLAMP/HIGHZ (voltage test)
RUNBIST (built-in self test)
…
(slow!)

## Slide 13
JTAG variations
Manufacturer | Processor family | Debug interface | #pins
Atmel | AT91 ARM Thumb | JTAG | 4
Atmel | megaAVR | JTAG | 4
Atmel | tinyAVR | debugWIRE | 1
Silicon Labs | 8051 (small) | C2 | 2
Silicon Labs | 8051 (larger) | JTAG | 4
Zilog | eZ80 | ZDI | 2
Freescale | MC68HC12 | BDM | 1
Freescale | MPC500 | Nexus 5001 | 16
ST Micro | STR710 ARM | JTAG | 4
LSI Logic | MiniRISC MIPS | EJTAG | 4
Toshiba | TX system MIPS | EJTAG | 4

## Slide 14
On a development board

## Slide 15
On a product
through-holes
header

## Slide 16
Low-level (non-processor chips)
Software interface
High-level IDE for processor
programming and debugging
Custom, anything in-between