## Slide 1: Measuring Digital System Latency from Sensing to Actuation at Continuous 1 ms Resolution
Weixin Wu, Yujie Dong, Adam Hoover
Dept. Electrical and Computer Engineering,
Clemson University

## Slide 2
What is system latency
Delay from when an event is sensed to when the computer “does something” (actuates)
Examples: camera to display; gyroscope to motor

## Slide 3
Why do we care?
If delay is constant, human users can adapt, machine systems can be built to specification
Time
Constant delay

## Slide 4
What if it is not constant?
May have some relation to “simulator sickness”; machines have to be built with a lot more tolerance for variability in delay
Time
Varying delay

## Slide 5: How do we measure it?
Components use asynchronous clocks; computer timestamps do not include sensing/actuation times or variability in buffers
Timestamp
Timestamp
unmeasured
unmeasured

## Slide 6: Indirect system latency measurement
Outside observer
Measure when the property being sensed/actuated are same
Example: marker position in “real world” matches marker position in “display”

## Slide 7: Previous works (camera based)
  Bryson & Fisher (1990)
  He, et. al. (2000)
  Liang, Shaw & Green (1991)
  Ware and Balakrishan (1994)
  Steed (2008)
  Morice et. al. (2008)
Sensor
Actuator
Outside observer

## Slide 8: Previous works (event based)
  Mine (1993)
  Akatsuka & Bekey (2006)
  Olano et.al. (1995)
  Morice et. al. (2008)
  Teather et. al. (2009)
Outside observer

## Slide 9
Why measure continuously?
Time
Average infrequent or irregular measurements
Measure:

## Slide 10: Continuous measurement
Outside observer is high speed camera
Can capture 480 x 640 image resolution at 1,000 Hz for up to 4 seconds

## Slide 11: Experiment 1: camera to display

## Slide 12: Sensor, object in “real world”
Bar is manually moved right to left in about 1 second

## Slide 13: As seen by outside observer
Bar position in display lags behind bar position in real world

## Slide 14: Automated image processing
Calculate P=(X-L)/(R-L) for both events

## Slide 15: Continuous latency measurement
Plot Ps and Pa for each high speed camera frame

## Slide 16: Result
Delay varies with 17 Hz oscillation, 10-20 ms magnitude
frequency
magnitude

## Slide 17: Result
Histograms, or averages, do not provide the whole picture

## Slide 18: Modeling the variability
The histogram of delay is uniform but NOT random

## Slide 19: Experiment 2: gyroscope to motor

## Slide 20: As seen by the outside observer
Bar on motor lags behind bar being manually rotated

## Slide 21: Automated image processing
Calculate theta for both events (relative to initial theta)

## Slide 22: Result
Similar high frequency/magnitude variability as in experiment 1

## Slide 23: Result
Lines are not parallel – lower frequency variability
Changes every trial, due to varying sensor error

## Slide 24: Fitting sinusoid to low frequency
Two examples:
Ten trials of 50 degree rotation in 800 ms:
  0.5-1.0 Hz variability in delay, magnitude 20-100 ms
Seven trials of 10 degree rotation in 800 ms:
  0.5-1.0 Hz variability in delay, magnitude 20-100 ms

## Slide 25
Conclusion
Measuring delay continuously at 1ms resolution shows interesting variations in latency
Relation to simulator sickness?
Next experiments: control latency variability, test its effect on people