Computer vision for computer games

Enhancing the experience…

Ajay Abraham

Dept. of Electrical Engineering, Clemson University, Clemson SC Email: ajaya@clemson.edu

Nitendra Nath

Department of Electrical Engineering,Clemson University,Clemson SC Email: nnath@clemson.edu

Keywords:	Computer games, Image Moments, Vision Input

Abstract:	Computer games have attracted a wide market over the past few years and their appeal may be further enhanced through vision based inputs.  The high speed and low cost requirements make system design challenging. The response time of the vision interface should be less than a video frame time and the interface should cost less than $50 U.S. The original authors developed specialised algorithms and hardware to make an integrated vision based gaming system using on-chip image processing. Their algorithms were based on Image Moments and orientation histograms. In this project, we seek to make the technology even more accessible to the point of being virtually freeware. The algorithms may be run on a PC and a web cam may be used for taking vision inputs for the player. The implementation was carried out using the Java Media Framework which takes care of communication with the USB web cam. We aim to interface the vision inputs with any of the common java applet games found on the Internet.

1	INTRODUCTION

The Computer games industry is fast emerging as a formidable contender in the world trade markets, grossing over 30 billion US$ last year alone. Game players find it captivating and challenging to engage with the computer (A.I.) via Joysticks, mouse or keypads.

All the above restrict hand motion to a few degrees of freedom and can become uncomfortable after an extended period of use. Using the natural unencumbered hand or body motions as control inputs to the game provides for a more comfortable and easy to use facility for playing games on the computer. The original authors [1] aimed to make to make an integrated vision based gaming system under 20$ with easily available hardware and fast response times of around 10ms. We have undertaken to use their algorithm on a commonplace configuration PC (800 MHz, 256MB, Intel Integrated Video Card) with a Logitech web cam. One of the main motivating factors behind this project was to make vision based gaming even more accessible by extending it to work on any PC with a web cam. Since currently almost every PC owner has a web cam, this would make the cost of installation almost zero.

Some features of Computer games lessen design difficulties. In most games, the user can exploit immediate visual feedback to reach the desired effect, ex. If the player is learning to make a turn in the game, and he/she sees that he/she isn’t turning enough, the player can relate the feedback from the game and the knowledge of body posture to modulate his responses. The vision system need merely track the (visual) center of mass of the player, but the game can turn that into running, jumping or crouching depending on game context.

Computer game applications represent a niche for high speed, low cost vision systems. The authors [1] developed hardware and algorithms for a vision system for the same niche. Our approach is to use the same algorithm on a PC with commonplace configuration and a web cam, and thus make the technology accessible to virtually anyone.

2	algorithm

In their original paper [1], the authors have used Image moments to obtain the visual centre of the body part as well as the orientation and degree of closeness to the aperture. We have restricted ourselves to just calculating the visual centre for the current evaluation stage. Image moments [2, 3] provide useful summaries of global image information, and have been applied to shape analysis of other tasks, often for binary images. The moments involve sums over all pixels, and so are robust against small pixel value changes. Within the structure of the computer game, they can also provide sufficient information for the computer to reliably interpret control inputs from the users body position.

If I(x,y) is the image intensity at position x,y, then the image moments, up to the second order are:

M00 = ∑x∑y I(x,y)

M11 = ∑x∑y xyI(x,y)

M10 = ∑x∑yxI(x,y)

M01 = ∑x∑y yI(x,y)

M20 = ∑x∑y x2I(x,y)

M02 = ∑x∑y y2I(x,y)

Xc = M10/M00    Yc = M01/M00

a = M20/M00 – Xc2

b = 2(M11/M00 – XcYc)

c = M02/M00 – Yc2

Θ = arctan(b, (a-c))/2

L1 = √( (a+c) + √(b2 + (a-c)2))/2

L2 = √( (a+c) - √(b2 + (a-c)2))/2

The extracted parameters are independent of the overall image intensity. In this project we are restricting ourselves to extracting only Xc and Yc, the coordinates of the visual centre of the hand.

3	implementation

This project was implemented on a PC with the following configuration:

Processor: Intel Pentium III

Memory: 128MB

CPU Speed: 800 MHz

Web cam : Logitech Quickcam Pro 4000

The project was initially started in VC++ with the Logitech sdk, but this was found to be supported only with driver version 5.4.3 and only on the 3000 series. Due to these limitations, the Java Media Framework (JMF) was chosen instead to be the channel for communication with the web cam.

Development in Java has lot of advantages:

Cross-platform operation

Dual usability as applet or stand alone application

Extensive development support

Native socket programming support

JMF is a simple and easy to use tool for registering media devices connected to the PC. It has a graphical interface for adding or removing devices, as shown below :

Once the web cam is registered as a video capture device, It can be accessed through objects derived from the JMF classes which have been installed.

The application is being developed as a standalone Java application. It may also be developed as an applet to be used by anyone accessing the page the applet is on, but as of now, running the applet requires installation of JMF. Thus, a standalone application would serve just as well.

The GUI was constructed using Java Swing. Threads were used to handle GUI events and frame capturing.

4	Results

Currently we are able to approximate the visual center of the hand. The next stage would be to interface the application with a rudimentary game and refine it thereof. The application currently does not run at optimal speed owing to the memory consumption while writing images. The delayed response is as of yet unavoidable as pixels may be accessed only after the image has been stored.

Brian Postma’s breakout applet is a good candidate for interfacing with the inputs from the web cam. Since the applet is also written in Java, the design problem is simplified.

5	further extensions

·	Interface various games with the applciation

·	Writing the application as an applet would simplify its use as the player need not have jdk installed to run the program

·	Multiplayer capabilites maybe possible with Java Servlets

6	conclusions

The algorithm from the original authors was implemented on a PC equipped with a webcam. One significant limitation is that a sharp contrast between the body part and the environment is required. This translates to the user being in either a brightly lit room or against a dark background.

The response was visibly slower than as required by the authors[1]. Although more computing power is available in a common PC, it is much less efficient than specialised hardware. Also, since pixel computations were performed on the fly using an AR chip, a much faster response time was obtained by the authors while using an integrated system.

Java, being the language of the Internet, has many advantages as the choice for development, the foremost being open source code bases. There are extensive code samples and java software in varied fields. The application maybe extended to being played online by making it an applet or it maybe extended to multiplayer games through the use of Java Servlets.

7	references

1.	Freeman, Tanaka , Ohta and Kyuma,  Computer Vision for Computer Games, IEEE Conf. On Automatic Face and Gesture Recognition October 1996

2.	B.K.P. Horn Robot vision MIT Press

3.	D.H. Ballard and C.M. Brown, editors, Computer Vision, Prentice Hall

4.	The Java Tutorial, java.sun.com/doc/books/tutorial