## Slide 1
Zuo Zhou1, David A. Ladner1, Negin Kananizadeh1, Sapna Sarupria1, Scott M. Husson1, Illenia Battiato2,
1Clemson University
2Stanford University
Concentration polarization modeling for reverse osmosis membranes with engineered surface features

## Slide 2
Overall Approach

## Slide 3
Motivation from experiments

## Slide 4
Membrane: Polyamide thin-film composite nanofiltration membrane.
Line & groove silicon stamp
Thermal embossing
Nanoscale patterning
PEGDE (5 wt% and 15 wt%)
Reaction
Chemical coating

## Slide 5
Weinman & Husson, Journal of Membrane Science 513 (2016) 146–154

## Slide 6
Modeling methods

## Slide 7
This research is to study concentration polarization (CP) on patterned membranes.
The goal is to learn the mechanisms behind CP development.
Goals
membrane
membrane
Notes: Editorial Guidelines on Bullets:
1. Vertical lists are best introduced by a grammatically complete sentence followed by a colon. No periods
are required at the end of entries unless at least one entry is a complete sentence, in which case a period
is necessary at the end of each entry.
Example: A university can be judged by three measures:
· The quality of its students
· The quality of it faculty
· The quality of its infrastructure
2. If a list completes the sentence that introduces it, items begin with lowercase letters, commas or semicolons
(if individual items contain commas) are used to separate each item, and the last item ends with a period.
Note that the introductory clause does not end with a colon.
Example: A university can be judged by
· the quality of its students,
· the quality of its faculty,
· the quality of its infrastructure.
3. Avoid mixing sentence and nonsentence items in a bulleted list.
7

## Slide 8
Model Introduction
Introduction
  Computational fluid dynamics (CFD) uses numerical analysis to analyze fluid flow problems.
  All the models are built with COMSOL Multiphysics (version 5.3).
Governing equations
Conservation of momentum
Conservation of mass
Convection diffusion

## Slide 9
Laminar flow
Convective-diffusion
Name | Value | Description
A | 5.24·10-12 [m/(s·Pa)] | Permeability coefficient
fos | 4872[Pa·m3/mol] | Osmotic coefficient
Parameters
Feed boundary
0.1m/s
Inflow concentration: 25 mol/m3
Concentrate boundary
2800 kPa
Permeate: A(Δp-Δπ)
π=fosC
3D Conceptual Model

## Slide 10
Patterns
(a)
(b)
(c)
(d)
(e)
(f)
(g)
(h)

## Slide 11
Feature Length, l (µm) | Feature Height, h (= 0.5·l) (µm) | Between-Feature Distance, d (= l) (µm) | Total Length, L (µm) | Total Width, W (µm)
2 | 1 | 2 | 16 | 8
8 | 4 | 8 | 64 | 32
32 | 16 | 32 | 256 | 128
128 | 64 | 128 | 1024 | 512
512 | 256 | 512 | 4096 | 2048
Pattern Sizes

## Slide 12
Pattern length: 2 µm
Pattern length: 8 µm
Pattern length: 32 µm
Pattern length: 128 µm
Pattern length: 512 µm
Pattern Sizes

## Slide 13
CP Factor
The Concentration Polarization Factor (CP factor) can be defined as a ratio of salt concentration at the membrane surface (Cm) to bulk concentration (Cb).
Flat 512 membrane CP factor = 1.86
Concentration profile
mol/m3
m/s
Velocity profile

## Slide 14
Velocity Normalization

## Slide 15
Numerical Solutions without Velocity Adjustment

## Slide 16
Numerical Solutions vs. Sherwood Correlation
Sherwood correlation

## Slide 17
CP Results

## Slide 18
Normalized CP Factor

## Slide 19
Streamlines

## Slide 20
Permeate Flux Results
m/s

## Slide 21
Normalized Permeate Flux

## Slide 22
L
z
h=256 µm
Definition of Roughness
L = evaluation length
= the profile height function
Roughness = 128 µm
Roughness normalized to pattern height = 128 µm/256 µm = 0.50
Roughness = 103 µm
Roughness normalized to pattern height = 103 µm/256 µm = 0.40
Roughness = 84 µm
Roughness normalized to pattern height = 84 µm/256 µm = 0.33

## Slide 23
Roughness vs. Boundary Layer Thickness
Roughness normalized to pattern height: total roughness (Ra) projected to pattern height.
Boundary layer thickness (BLT): BLT is calculated through diffusion coefficient and mass transfer coefficient.

## Slide 24
Roughness vs. Average Boundary Layer Thickness

## Slide 25
Conclusions
Lower average shear stress gives higher CP.
In general, adding patterns does not decrease CP.
  The fouling mitigation seen in experiments is likely due to other factors.
Adding patterns increased roughness, and therefore decreased mass transfer coefficient and increased boundary layer thickness.

## Slide 26
Future Work
Future studies will also use particle tracing.

## Slide 27
Overall Approach

## Slide 28
Peng Xie, Clemson U.
Rasna Sharmin, Clemson U.
Illenia Battiato, Stanford U.
National Science Foundation
Grant No. CBET-1236070
Grant No. CBET-1534304
Acknowledgements

## Slide 29
Supplemental Materials
Flat | LG Rectangle | LG Trapezoid | LG Triangle | LG Circle | Rectangular pillar | Pyramid | Circular pillar
1.56E-05 | 1.11E-05 | 1.22E-05 | 1.32E-05 | 1.25E-05 | 1.08E-05 | 1.39E-05 | 1.18E-05
Flux for each geometry (m/s)
Constant flow: all the 512 um models maintain the same total flow: 1.31E-10 m3/s.