## Slide 1: Computational modeling to improve chlorinator design in a Haitian drinking water system
Ashley Martin, Colby Cash, and David A. Ladner
AEESP Conference, Tempe, Arizona. May 16, 2019

## Slide 2: Clemson Engineers for Developing Countries (CEDC) has worked in Cange, Haiti, since 2009.

## Slide 3: A hydraulic pump sends water up the canyon and through a treatment system.
Notes: EDUSC: episcopal diocese of upper south Carolina:
1000 feet to the treatment building. More to the cisterns.
4000 people

## Slide 13: Chlorination has taken several forms at different times.

## Slide 15: The most recently installed chlorinator is a tablet feeder built to handle the high system pressure (>100 psi).
Notes: AKA erosion chlorinator.

## Slide 16: Residual chlorine measurements are taken every other day.

## Slide 18: Achieving stable chlorine concentrations has been challenging.
Notes: 2009: Jeff Plumbly started the work on treatment system
2013: cartridge filters and UV. Treatment (chlorination; accutab)
June 2014: built water testing lab
June 2014: Accutab (didn’t work well)
June 2015: tablets inserted in the old filter housings

## Slide 19: We are investigating mass transport within the tablet feeder to achieve consistent chlorine doses.
Flow through the chlorinator
Dissolution of chlorine tablets
Transport of free chlorine

## Slide 20: Mathematical Model
Conservation of Mass
Conservation of Momentum
Dissolved Mass in Fluid
Important Boundary Conditions
  Higher initial concentration at tablet surface
  Inlet
  Outlet
Initial Conditions
  No initial concentration in chlorinator

## Slide 21: COMSOL Model
Laminar Flow Physics
Transport of Diluted Species Physics
Moving Mesh

## Slide 22: COMSOL Model
Laminar Flow
Inlet
Normal inflow velocity
Outlet
Zero Pressure
All remaining lines set as walls
Run in Stationary Model

## Slide 23: COMSOL Model
Transport of Diluted Species
Inlet
Normal inflow velocity
Outlet
Zero Pressure
All remaining lines set as no flux boundary
Concentration
1 mol/m3
Diffusion Coefficient
1E-9 m2/s
Run in Time Dependent Model

## Slide 24: COMSOL Model

## Slide 25: COMSOL Model

## Slide 26: 2D and 3D give similar results, though 2D has fewer degrees of freedom for chlorine flow.

## Slide 27: Tablet dissolution is modelled with a moving mesh.

## Slide 28: We compared simulations with 1, 3, and 5 tablets.

## Slide 29: Chlorine concentrations peak early then taper off over time.

## Slide 30: We changed the inlet and outlet locations to explore benefits to chlorine dose stability.
1
2
3
4
5
6
7

## Slide 31: Scenario 5 (inlet and outlet above tablets) gave most consistent chlorine levels.

## Slide 32: With less fluid flow directed at the tablets, convection plays a smaller role than diffusion. Tablet surface area is less important.

## Slide 33: Acknowledgements
Clemson Engineers for Developing Countries (CEDC)
  David Vaughn
  Paris Stringfellow
  Jeff Plumbley
Larry Murdoch