## Slide 1: Lab space etiquette
Dr. Dean’s Lab
Rhodes 515

## Slide 2: Lab Tools
Pipettes
  Use the right size for what you need to measure
  Don’t over pull liquids - don’t keep using the pipette if you get liquid in the filter
  Use a new tip for anything new, or anytime the tip touches anything
  Plug the guns back in when you’re done
  Tips go in the bin behind biohazard bin
Scales
  Zero first – with a tray if you’re measuring something dry
Water Bath
  Never fully submerge anything – use trays or test tube racks
  Use weights to keep bottles from floating up
Filter system
  Use the one in the tissue culture lab on the fourth floor (416 back room)

## Slide 3: Lab Equipment
Bio-Hood
  STERILE! – you have to use proper aspectic technique
  Always have a waste container – keep it separate from anything clean
Chemical Hood
  NOT STERILE
  For anything with potentially dangerous fumes
Dissection Hood
  NOT STERILE
  Make sure the fan is on
  Let the fan run for 10-15 minutes before and after dissection
Incubator
  CLEAN! - you have to use proper aseptic technique
  Sign the sheet on the door
  Double check that the inner door is closed and latched

## Slide 4: Aseptic technique
Gloves
  Take off rings that could cause tears
Lab Coats
No exposed skin!
  Be careful of watches, hair ties, bracelets etc.
Spray everything down with 70% ethanol
  Wipe things dry with a kimwipe
  Do not spray the filter on a flask with a filter cap.
Open things inside the hood
General note: glass ware isn’t sterile because we don’t autoclave it
Every time you go into the Bio-hood or Incubator
  This is so crucial to minimize contamination risk and keep everything sterile and alive

## Slide 5: Dissections
All dissections in the dissection hood!
Keep everything in the biohazard bag or on the dissection mats
  Keep joints on ice in Styrofoam
Always turn on the hood before you start
  Make sure the fan is on
Smaller pieces
  Easier to keep alive
  We’ll be standardizing
Always tendon wash and media rinse
Spray down the joints with ethanol while you go
Cut tendon ends
  That’s where contamination happens

## Slide 6: biohazard
Bin vs. Freezer?
  Bin:
    gloves that touched tendons, petri dishes, empty flasks etc.
    No liquids!
  Freezer:
    joints after dissection, pieces of tissue, blood
    Has to be frozen for 24 hours
    Has to be in a red bag
    Label and put in the drawer
Liquid waste gets put in the waste container
  Squirt bleach from bottle by sink
  Pour in 4-L beaker then rinse

## Slide 7: Clean up
Dishes
  Rinse everything out and put it in the first bin
  NEVER put metal in the second container
Surfaces
  Spray with ethanol and wipe with kimwipe
Sharps (like disposable scalpel blades)
  Put in the sharps container by the water bath
Broken Glass
  Broken glass container by the CO2 tanks
1
2

## Slide 8: Putting things away
LABEL EVERYTHING!!!
  Everything has to have:
    Your name (or initials)
    The date
    What it is
    Project or CI name
Make a note in your lab notebook – what and where it is
Don’t leave anything on counters or in the bio-hood

## Slide 9: More General Things
If we run out of something? Tell whoever is in charge of your lab time or request it on Quartzy!
  *As a general rule, it is always okay to ask any of the grad students (Hannah, Aniqa, Nardine, Scott, Michael, Liv) for help if you need it or have a problem and they are in the lab
Leave backpacks outside
  No food in the lab
Keep surfaces clear
Keep cabinets and fridge closed
When you leave, turn off the lights, lower hood sashes, and turn off hood lights
Remember that we are sharing this space!!