## Slide 1
Manufacturing the Bite Counter
Adam Hoover
Electrical & Computer Engineering Department

## Slide 2
Embedded System Design
Laboratory
experiments
(2007)
1st gen (2011)
($35k + labor)
2nd gen (2015)
($125k + labor)

## Slide 3
Breadboarding and Parts Selection
gyroscope
LCD
processor
battery, holder
charger
I/O (buttons, speaker, vibratory motor, USB port)

## Slide 4
Processor
Texas Instruments MSP430 selection guide
MSP430 family chosen because:
LCD driver built-in
I2C bus (connect to sensor chip)
Low-power (nothing unusual, all microcontrollers are low power)
Small program and data (<16 KB)
Inexpensive (appx $1 per part in bulk)
Legacy (used in version 1 and version 2)

## Slide 5
Programming Development
development board ($50-150)
dev board JTAG-USB
USB connects to PC
connects to dev board
insert chip here

## Slide 6
Sensors
1st gen analog circuits and sensor chip
2nd gen digital chip

## Slide 7
LCD
1st gen off-the-shelf LCD and dev surfboard
2nd gen custom LCD design
top row 7 seg (values), bottom row 16 seg (units)

## Slide 8
LCD connection to PCB
Pins have to be individually soldered (lots of work)
Pins take up space (bad for small devices)
space needed underneath

## Slide 9
Zebra Strip (Elastomer Conductor)
PCB
LCD
zebra strip
support
conductor
insulator

## Slide 10
Battery
1st gen used coin package
(consumer industry)
2nd gen used square package
(wearables industry)

## Slide 11
Design Team
Prototypes
Circuit diagrams

## Slide 12
Design stages
Circuit diagrams
Printed circuit board (PCB) designs

## Slide 13
Design stages
PCB designs
PCB manufacturing

## Slide 14
Pick-and-Place PCB Assembly Demo
part reels

## Slide 15
Bite counter PCB (1st gen)
gyroscope
processor
LCD
battery
USB port
USB-RS232 bridge
speaker
buttons
JTAG
charger

## Slide 16
Bite Counter PCB (2nd gen)
sensors
processor
LCD
speaker
buttons
JTAG
charger
USB

## Slide 17
Case Design
Industrial designer
$10k (2nd gen)

## Slide 18
Mold and Case Manufacturing
Molds cost $10k (1st gen), $40k (2nd gen)

## Slide 19
Injection Molding Demo

## Slide 20
Design Team
Molding and case production
Industrial designer

## Slide 21
Device Assembly
PCB, case, battery, LCD, zebra strips, screws, watchband, packaging
product

## Slide 22
Manufacturing Startup Costs
Part | Manufacturer | Required tooling | Cost (appx)
PCB | AAPBC | Screening, layout | $2,000
LCD | Varitronix | Design, screening | $8,500
Case | EHI | Design | $10,000
Mold, Case | Five Star Plastics | Mold design, build | $50,000
Packaging | Yebo | Design, layout | $5,000
All these are one-time costs

## Slide 23
BOM (Bill of Materials)
Part | Manufacturer | Part# | Oder size | Cost/piece
PCB | AAPBC | AE102140-003 | 1000 | $36.00
Zebra strips (2) | Fujipoly | 2004-080 867L 146 H | 2500 | $0.30
Battery | EVE | P0510-LF(281418) | 1000 | $3.70
LCD | Varitronix | VL_7268_V01 | 5000 | $1.10
Case bottom | Five Star Plastics |  | 960 | $1.18
Case top | Five Star Plastics |  | 960 | $1.92
Screws (4) | MSCdirect.com | #78079787 | 4200 | $0.43
USB cable | Cableleader.com | U2103-1103 | 1200 | $0.85
USB charger | DHGate.gom | #215650707 | 1200 | $1.05
Watchband/pins | Voguestrap | TX1820BK | 1200 | $3.75
Packaging | Yebo |  | 10000 | $1.20
Cost per device appx $53
(separate BOM, 29 parts)

## Slide 24
Batteries – Bulk
400-500 batteries per box

## Slide 25
Battery Installation
solder points
after soldering, battery rests on PCB

## Slide 26
Battery Tests
Function | current (mA)
accelerometer maximum | 0.450
accelerometer 30 Hz | 0.019
gyroscope maximum | 3.2
gyroscope 30 Hz | 3.0
CPU maximum | 0.220
LCD off | 0.016
LCD fully lit | 0.019
speaker | 0.2
45 mAh battery lasts 25 days in watch mode;
10 days with regular daily usage of bite counting

## Slide 27
PCB Programming with Jig Tool
USB connects to PC
PCB goes here
JTAG pins
spring lever

## Slide 28
PCB (Front and Back)
LCD pads
JTAG pads

## Slide 29
Memory Space
Addresses | Content
C000-C3FF (1 Kb) | resident monitor
C400-F3FF (12 Kb) | application code
F400-FFE0 (3 Kb) | data records
FFE0-FFFF (32 bytes) | interrupt table
Monitor code allows device to be reprogrammed in-the-field (from PC)
Application code operates the device functions
Data records store bite count records each time device is used; can be uploaded to server if device plugged into PC
Interrupt table stores vector of addresses into application code (e.g. for button presses)

## Slide 30
Cases
2 parts (front, back)
100 cases per box

## Slide 31
Displays – Bulk
400-500 LCDs per box

## Slide 32
Zebra Strip (Elastomer Conductor)
bag of 1000
small
case holds everything together

## Slide 33
PCB in Case
LCD pads

## Slide 34
Products
ready for charging and packaging

## Slide 35
Package Design
Package design and manufacturing

## Slide 36
Packaging – Pre-assembly
box assembled with origami-style folding
100-200 boxes

## Slide 37
Test and Debug Parts
devices that fail during testing
parts that fail during assembly
customer returns