## Slide 1: A device to record natural daily wrist motion
MS Thesis Defense
Surya Prakash Sharma
Committee Members:
Dr. Adam Hoover (Chair)
Dr. Ian Walker
Dr. Jason Hallstrom
November 24, 2014
Notes: Hello and welcome
Titled “A device to record natural daily wrist motion”
Grab some snacks

## Slide 2: Outline
Motivation and Background
Methods
Results
Conclusion
Notes: We’re going to discuss
Why
How
What were the results
What did we learn

## Slide 3: Motivation
Our vision: Wrist-worn eating activity monitor
Previous work: 81% accuracy detecting periods of eating (44 subjects, 1 day) 86% accuracy counting bites during eating (49 subjects, 1 meal)
Need: device to record large number of people for long period of time
The bite counter
Notes: Create wrist worn eating activity monitor
Work done by our group previously attained 81% accuracy when trying to detect periods of eating
Further they could count the number of bites during these meals with 86% accuracy
Our group now needs more data to improve these algorithms, for which we plan to create a device to record wrist movement across a large number of subjects for a long period of time.

## Slide 4: Background (cont)
Recording wrist movement data requires three basic components
Accelerometer – Translational motion
Gyroscope – Rotational Motion
Memory – Store Data

## Slide 5: Background
Multiple wrist worn devices available.
None has addressed the need of recording translational and rotational wrist movement data.
Many devices do not contain all the required sensors
Others have unneeded features increasing cost, weight and discomfort, while reducing battery life.
Notes: Multiple devices already exist.
They process movement data and record some other quantity (steps)
Most devices missing gyroscope.
Unneeded features.

## Slide 6: Previous Work
iPhone Based Data Logger
  Long Battery Life
  High resolution data
  High customizability
  Big Size
  Low comfort
http://www.ces.clemson.edu/~ahoover/theses/dong-diss.pdf

## Slide 7: Other Devices
Activity Trackers
  Long Battery Life
  Small Size
  High Comfort
  Economical Cost
  Low resolution data
  No customizability
  No gyroscope
https://www.flickr.com/photos/uscpsc/13104103473
The Fitbit Flex

## Slide 8: Other Devices (cont)
Research Devices
  Average Battery Life
  High resolution Data
  High customizability
  Medium Comfort
  High cost
  Development Kit: $2000
  Unit : $249
www.shimmersensing.com/shop/shimmer3
Promotional photo of the SHIMMER

## Slide 9: Other Devices (cont)
Smartwatches
  Average Battery Life
  Average customizability
  OK Comfort
  Some have all sensors
  High cost
  Unit : $249
  Low resolution data
https://www.flickr.com/photos/ridble/12794729274/in/photostream/
Samsung Gear 2

## Slide 10: Summary
Name | Market Segments | Both Sensors | Size | Weight (g) | Active Battery Life (hours) | Extra components
iPhone | Mobile Phone | Y | Large | 149 | 40 | Display, GSM Module
MetaWatch | SmartWatch | N | Small | 81 | 80 | Display, Bluetooth Module
Samsung Gear 2 | SmartWatch | Y | Small | 68 | 48 | Display, Bluetooth Module, Media Player
Fitbit Zip | Fitness Tracker | N | Small | 8 | 6 mo | 
Fitbit Flex | Fitness Tracker | N | Small | N/A | 120 | 
Jawbone Up Move | Fitness Tracker | N | Small | 6.8 | 168 | 
Jawbone Up 3 | Fitness Tracker | N | Small | 29 | 168 | 
Fitbit One | Fitness Tracker | N | Small | 8 | 240 | 
Nike FuelBand | Fitness Tracker | N | Small | 30 | 96 | 
SHIMMER | Research | Y | Medium | 23.6 | 24 | SD Card, Bluetooth Module
Thalmic Labs Myo | Research | Y | Medium | 93 | 48 | EMG Sensors
Note: Sizes are as follows:
Small : Wrist watch or similar
Medium: Larger than wrist watch, smaller than a smartphone.
Large: Smartphone

## Slide 11: Novelty
New Wrist mounted device to log motion data
  Good Battery Life
  High customizability
  Economical Cost
  High Comfort
Smaller size leads to more comfort, and the user can wear it longer

## Slide 12: Methods
http://www.ti.com/graphics/folders/partimages/MSP430F248.jpg https://www.flickr.com/photos/40875537@N04/5659910644
http://www.snowcap.fi/uploads//2011/12/mpu6000.png http://electronics-diy.com/img/FT232RL_chip.jpg
http://www.mouser.com/images/adestotechnologies/images/cason8.jpg
Sensors
Microcontroller
Memory
USB to UART
Computer

## Slide 13: Components
    Sensor
    Memory chip
    Microcontroller
    USB to UART bridge
    Battery
    Battery charger
    LED
    Button
    Case

## Slide 14: Procedure
    Part selection
    Circuit design / Prototype / Programming
    PCB design
    Soldering

## Slide 15: Sensor
MPU-6000: MEMS 6 axis sensor
2.375 – 3.46 V supply
Current Consumption:
Accelerometer : 200 uA
Gyro + Acc: 3.8 mA
Digital Communication over SPI / I2C
8 KHz internal clock
Measurement Range:
  Accelerometer: ±2, ±4,±8,±16 g
  Gyro: ±250/±500/±1000/±2000 °/sec
Breakout Board
Current Consumption for STMicro LSM330: 6.1 mA
InvenSense MPU-6000
https://www.sparkfun.com/products/11234
http://www.ebay.com/itm/261417344740
Notes: Prev work: 3 components, 1 acc, 2 gyro.
Each gyro 6.1 mA
Gyro + Acc 3.8 mA
St Micro 6.1 mA
33% power savings just by using the right component
Breakout Board
Not meant to be used in prototypes. Meant for small handheld devices like phones.
Smaller and smaller.
Hard to connect to these.
Breakout boards breaks the pads on the chips to bigger holes to connect to.
BB was imported from Germany b/c none available here.
BB for sister component was available, but that chip lacks SPI.

## Slide 16: Microcontroller
MSP430F248
1.8 – 3.46 V supply
Current Consumption : 270 uA @ 1 MHz
SPI and UART modules
Two 16 bit timers
4 KB RAM
The MSP430F248 microcontroller
Notes: Looked at previous work / competitors and selected the MSP430 fam.
400 devices.
We knew it would need to support the memory and the sensor.
SPI
Timer

## Slide 17: Memory
AT45DB642D
2.7 – 3.6 V supply
Current Consumption
  Read : 15 mA
  Write / Erase : 25 mA
  Standby : 25 uA
SPI communication
Package : CASON
Write duty cycle: 0.56%
Average current: 140 μA
Memory chip
Notes: High write current
Writes once every 11 seconds, takes about 64 milli
SPI

## Slide 18: SPI
SPI master with two slaves on the same bus
Sensor
Memory
http://en.wikipedia.org/wiki/Serial_Peripheral_Interface_Bus

## Slide 19: Data Transfer
FT232RL USB to UART bridge
5 V supply
Integrated 3.3 V level converter
Data transfer technology would require 18 mA of current over 30 minutes
Using a wired connection allows this power to be sourced from the host
Battery can be charged with the same connector
Allows us to get data off the device
FT232RL
https://www.sparkfun.com/products/650
Notes: Once data is recorded the entire day, has to be transferred to a computer.
Computers lack serial ports, replaced by the newer USB standard.
FT232 creates a virtual serial port on the computer through the USB connection.
Why not wireless.
18 mA wireless, 30 minutes time, need battery power.
Wired lets us source this from host.

## Slide 20: LED
Typical current draw of 20 mA
Duty cycle: 0.56%
Average current: 110 μA
Off the shelf LED
Photo of a LED

## Slide 21: Case
Ergo Minitec Series
Largest case used for previous work
Smallest case measures 52 mm x 32 mm x 15 mm
Intermediate ring allows a strap to pass through
Lightweight
Ergo Minitec Series Cases
http://www.okw.com/en/Plastic-enclosures/Minitec.htm

## Slide 22: Battery
Top view profiles of different batteries considered
Turnigy Nano-tech 160 mAh
Most batteries would fit in 52 mm x 32 mm
Case is limiting factor
Case is curved so the Duracell AAA 800 mAh, Nano-tech 300 mAh and LIR2450 90 mAh batteries wouldn’t fit
Nano-tech 160 mAh provides the highest battery capacity

## Slide 23: Prototype

## Slide 24: Programming
Simplified algorithm for the device

## Slide 25: Programming (cont)
MSP430 JTAG Tool
Photo: Texas Instruments

## Slide 26: PCB Layout
Parts placed before routing

## Slide 27: PCB Layout (cont)
PCB layout after routing

## Slide 28: Soldering (Mounting Parts)
Video : Soldering Crystal (41 seconds)

## Slide 29: Soldering (cont)
Video : Soldering SMD Resistor (44 seconds)

## Slide 30: Z – axis tape
Z – axis tape reel
Z – axis tape under a microscope
http://www.adafruit.com/product/1656
https://www.sparkfun.com/products/12042

## Slide 31: Soldering (cont)
Solder paste application
Stencil placement
Hot plate reflow soldering
https://www.sparkfun.com/tutorials/59
https://www.youtube.com/watch?v=P7Fa-WZHxbI
https://www.youtube.com/watch?v=1RMtOAHbfvU

## Slide 32: Final Device
Final PCB with top case cover

## Slide 33: Results
Final device mounted on wrist

## Slide 34: Results (cont)
Battery life of active device

## Slide 35: Results (cont)
WristView showing recorded data

## Slide 36: Results (cont)
WristView showing smoothed data

## Slide 37: Results (cont)
Device production cost

## Slide 38: Results (cont)
Name of Device | Market Segments | Both Sensors | Size | Weight | Active Battery Life (hours) | Extra components
iPhone | Mobile Phone | Y | Large | 149 | 40 | Display, GSM Module
MetaWatch | SmartWatch | N | Small | 81 | 80 | Display, Bluetooth Module
Samsung Gear 2 | SmartWatch | Y | Small | 68 | 48 | Display, Bluetooth Module, Media Player
Fitbit Zip | Fitness Tracker | N | Small | 8 | 6 mo | 
Fitbit Flex | Fitness Tracker | N | Small | N/A | 120 | 
Jawbone Up Move | Fitness Tracker | N | Small | 6.8 | 168 | 
Jawbone Up 3 | Fitness Tracker | N | Small | 29 | 168 | 
Fitbit One | Fitness Tracker | N | Small | 8 | 240 | 
Nike FuelBand | Fitness Tracker | N | Small | 30 | 96 | 
SHIMMER | Research | Y | Medium | 23.6 | 24 | SD Card, Bluetooth Module
Thalmic Labs Myo | Research | Y | Medium | 93 | 48 | EMG Sensors
This Work | Research | Y | Small | 26.6 | 24 | 
  Good Battery Life
  High customizability
  Economical Cost
  High Comfort

## Slide 39: Challenges
Microcontroller after cutting pins to desolder

## Slide 40: Future Work
Dataset of wrist motion movement needs to be created
100 – 200 subjects wearing this device for up to 2 weeks each
20 – 25 devices needed

## Slide 41: Future Work (cont)
Add a local time feature to the watch
Consider using EMG sensors to pursue new algorithms
Try a different profile with custom molded case

## Slide 42: Questions ?
Old people used to write obnoxious thinkpieces about how people these days always wear watches and are slaves to the clock, but now they've switched to writing thinkpieces about how kids these days don't appreciate the benefits of an old-fashioned watch. My position is: The word 'thinkpiece' sounds like a word made up by someone who didn't know about the word 'brain'.
http://xkcd.com/1420/