## Slide 1: Mobile robot navigation for person following in indoor environments
Committee Members:
Dr. Tim Burg
Dr. Stan Birchfield
Dr. Ian Walker
Dr. Damon Woodard
Ninad Pradhan
Ph.D. Dissertation Defense
July 25 2013

## Slide 2
Mobile robot navigation for person following in indoor environments
Mobile robot navigation in indoor environments
Person following in indoor environments
Workspace representation
Path planning
Robot control
Follower classification
Leader detection and tracking
Map generation

## Slide 3
Person followers
Service robots
Vacuum cleaners
Restaurant servers
Laundry robots
Luggage transporters
“Robots which operate in human-populated environments and assist humans in daily activities”.

## Slide 4
Person following
Telepresence
Speech recognition
Service robot
Museum tour guide
‘Rhino’ – Buhmann (1995)
‘Minerva’ – Thrun (2000)
Home patient care
‘Flo’ – Roy (2000)
‘CompanionAble’ – Gross (2011)
Home oxygen therapy
‘Hein II’ – Tani (2011)
Assistive personal robots
‘Grace’ – Kirby (2007)
‘Care-o-bot’ – Reiser (2009)

## Slide 5
Person following
Chen (2007)
Feature tracking
Disparity based segmentation
Motion segmentation
Brookshire (2010)
HOG person detection
Stereo estimation for depth
Outdoors person following
Doisy (2012)
Pan-tilt robot head mechanism
Kinect skeletal tracker
Stationary obstacle path planning
Miura(2010)
Short term occlusions
Laser map generation
Stereo based tracking
Yoshimi (2006)
Color based identification
Obstacle avoidance
Occlusion handling
Gross (2011)
Telepresence
Complete indoor map
Emergency event detection

## Slide 6
Person following
Robot follower
Human leader
From Yoshimi (2006):
Initialize to the leader
Follow the leader at his/her pace
Avoid obstacles
Resume contact with leader after occlusion

## Slide 7
Human leader
Classification system
Fully cooperative leader
Independent leader
Partially cooperative leader
Patient leader
Ensures zero occlusions.
Creates exact path for robot
Ensures zero obstacles between leader and robot
Ensures zero occlusions.
Expects path planning for stationary obstacles.
Ensures all obstacles are low height and stationary.
Makes no effort to avoid occlusions.
Makes no effort to stay within sensor range.
Waits for robot to overcome occlusions.
Makes no effort to avoid occlusions.
Does not wait for robot to overcome occlusions.
Expects high level communication with robot.
Research contribution

## Slide 8
Classification system
Fully cooperative leader
Independent leader
Partially cooperative leader
Patient leader
Chen (2007)
Kirby (2007)
Brookshire (2010)
Yoshimi (2006)
Doisy (2012)
Miura (2010)
Satake (2009)
Weinrich (2012)
Gross (2011)
Level 1
Level 2
Level 3
Level 4

## Slide 9
Level 3
Leader expectations
Leader does not create a path for the robot to follow.
Leader walks in an environment with stationary and moving obstacles.
System requirements
Leader does not make an effort to avoid occlusions.
Leader does not make an effort to stay within sensor range.
Control robot motion to handle occlusions.
Establish and verify leader identity.
Create a map to establish a workspace for path planning.
Plan a robot path around stationary and moving obstacles.
System modules

## Slide 10
System modules
Research contribution
Indoor environment
Kinect RGB-D sensor
Pioneer P3-AT robot
Leader tracking
Kinect skeletal tracker
Appearance descriptor generation
Leader detection, occlusion inference
Mapping
Floor occupancy detection
Manhattan rotation
Local environment map generation
Translation estimation
Navigation
Control input generation
Workspace generation
Predictive fields navigation

## Slide 11
Leader tracking
Kinect skeletal tracker
Appearance descriptor generation
Leader detection, occlusion inference
Leader tracking
Kinect skeletal tracker
Appearance descriptor generation
Leader detection, occlusion inference
Kinect depth image
Skeletal detection
Detection details
Tracking status of skeleton.
Skeleton center in 3D (mm).
Tracking status of joint.
Position of joint in 3D (mm).
Shotton (2011).
Depth-only detection.
Person and pose detection.
20 joints for pose, 19 bones.

## Slide 12
Leader tracking
Kinect skeletal tracker
Appearance descriptor generation
Leader detection, occlusion inference
Detection details
Research
contribution
RGB image
Skeleton overlay
Extracted bone patch
HSI color space
L*a*b* color space
Person Descriptor

## Slide 13
Leader tracking
Kinect skeletal tracker
Appearance descriptor generation
Leader detection, occlusion inference
Research
contribution
Person Descriptor
Occlusion types
Self-occlusion
Sensor range occlusion
Obstacle/person occlusion
Poor skeletal overlay
Bone angles to detect self-occlusion
Leader
Descriptor

## Slide 14
Leader tracking
Kinect skeletal tracker
Appearance descriptor generation
Leader detection, occlusion inference
Research
contribution
Occlusion types
Self-occlusion
Sensor range occlusion
Obstacle/person occlusion
Occlusion inference and recovery
Last position close to sensor range limit?
Self-occlusion
Sensor range occlusion
Bone angles okay?
Leader skeleton tracked?
Another descriptor matches leader descriptor?
Set as recovered leader
Obstacle/person
occlusion
Pause robot/ path planning
Pause robot/ path planning
Descriptor matches leader descriptor?
Follow person ‘exactly’
No
No
Yes
No
Yes
Yes
Yes
Yes
No
No

## Slide 15
Leader tracking
Kinect skeletal tracker
Appearance descriptor generation
Leader detection, occlusion inference
Occlusion inference and recovery

## Slide 16
Indoor environment
Kinect RGB-D sensor
Pioneer P3-AT robot
Leader tracking
Kinect skeletal tracker
Appearance descriptor generation
Leader detection, occlusion inference
Mapping
Floor occupancy detection
Manhattan rotation
Local environment map generation
Translation estimation
Navigation
Control input generation
Workspace generation
Predictive fields navigation
System modules

## Slide 17
Mapping
Floor occupancy detection
Manhattan rotation
Local environment map generation
Translation estimation
Mapping
Floor occupancy detection
Manhattan rotation
Local environment map generation
Translation estimation
Simultaneous Localization and Mapping (SLAM)
Plan a robot path to overcome occlusions?
What does the workspace look like?
Where is the robot located relative to the workspace?
Floor plane equation
Occupancy map
Estimate inter-frame translations and rotations

## Slide 18
Mapping
Floor occupancy detection
Manhattan rotation
Local environment map generation
Translation estimation
Estimate inter-frame translations and rotations
3-D correspondences
Scan matching
Direct 3D – Point cloud matching (ICP)
2D to 3D – Feature point matching
Too slow when matching entire point cloud
Inaccurate with sampled point cloud.
Unpredictable performance.
Too few features in some frames.
Poorly tracked features in some frames
Reasonable rotation estimates, though occasional failures were seen.
Poor translation estimates.

## Slide 19
Translation estimation
Mapping
Floor occupancy detection
Manhattan rotation
Local environment map generation
Estimate inter-frame translations and rotations
Research
contribution
Map initialization
Manhattan assumption
Wall planes are mutually orthogonal
Find reference lines and create mutually orthogonal bins
Total rotation relative to reference
No need for inter-frame correspondences
Inter-frame rotation estimate
Previously used by:
Peasley (2012)
Furukawa (2009)

## Slide 20
Translation estimation
Mapping
Floor occupancy detection
Manhattan rotation
Local environment map generation
Estimate inter-frame translations and rotations
Scan generation
Create a set of polar coordinate pairs relative to robot position
Robust line fitting to estimate a set of lines from scan data
Use inter-frame rotation model and RANSAC estimation
Total Manhattan rotation estimate
Multi-line RANSAC
Reference orientation

## Slide 21
Translation estimation
Mapping
Floor occupancy detection
Manhattan rotation
Local environment map generation
Total translation estimate
Robot motion input
Total Manhattan rotation estimate
Inter-frame translation estimate
Research
contribution

## Slide 22
Translation estimation
Mapping
Floor occupancy detection
Manhattan rotation
Local environment map generation
Total translation estimate
Research
contribution
Total Manhattan rotation estimate
Robot workspace map
Straight line map
T-junction map

## Slide 23
Indoor environment
Kinect RGB-D sensor
Pioneer P3-AT robot
Leader tracking
Kinect skeletal tracker
Appearance descriptor generation
Leader detection, occlusion inference
Mapping
Floor occupancy detection
Manhattan rotation
Local environment map generation
Translation estimation
Navigation
Control input generation
Workspace generation
Predictive fields navigation
System modules

## Slide 24
Navigation
Control input generation
Workspace generation
Predictive fields navigation
Navigation
Control input generation
Workspace generation
Predictive fields navigation
Leader unobstructed?
‘Exact’ person following
Predictive fields navigation
Yes
No

## Slide 25
Navigation
Control input generation
Workspace generation
Predictive fields navigation
Predictive fields navigation
Potential fields path planning
Navigation functions
Nonholnomic navigation functions
Khatib (1986)
Krogh (1986)
Arkin (1987)
Rimon and Koditschek (1990, 1991, 1992)
Tanner (2003, 2005, 2010)
Modified topology, gain tuning
Filippidis (2011,2012)
“Topological representation of the robot workspace in which the goal is the lowest point and obstacles are peaks. Goal attracts the robot, obstacles repel it.”

## Slide 26
Navigation
Control input generation
Workspace generation
Predictive fields navigation
Navigation functions
Predictive fields navigation
Research
contribution
Navigation functions
Can only be estimated for circular worlds.
Require non-circular worlds to be ‘star worlds’.
Require unknown shape transformation to map star world to a circular world.
Do not guarantee convergence for non star-world/circular workspaces
Predictive fields
Encapsulate practical workspaces using circular envelopes.
Do not need complicated transformations.
Retain all mathematical guarantees for arbitrary workspaces.
Similar to ‘union of ellipsoids’ by Tanner (2003)
‘Star-world’ transformations
Workspace representation

## Slide 27
Navigation
Control input generation
Workspace generation
Predictive fields navigation
Navigation functions
Research
contribution
Predictive fields navigation
‘Star-world’ transformations
Workspace representation
No moving obstacles
Elliptical fields representation
Rimon-Koditschek (1992) do not allow moving obstacles.
Chen (2005,2007) showed that moving obstacles could be used.
No incorporation of the sense of motion of obstacles.
Can take robot along a route with collision hazards.
Elliptical envelope represents direction and speed of obstacle.
Project obstacle along the major axis of its general ellipse.
Redefine obstacle repulsion function based on elliptical field.

## Slide 28
Navigation
Control input generation
Workspace generation
Predictive fields navigation
Navigation functions
Research
contribution
Predictive fields navigation
‘Star-world’ transformations
Workspace representation
No moving obstacles
Elliptical fields representation
Rimon-Koditschek (1992) do not allow moving obstacles.
Chen (2005,2007) showed that moving obstacles could be used.
No incorporation of the sense of motion of obstacles.
Can take robot along a route with collision hazards.
Robot stays out of path of collision hazard.
Moving obstacle model is useful in indoor populated environments.

## Slide 29
Navigation
Control input generation
Workspace generation
Predictive fields navigation
Navigation functions
Research
contribution
Predictive fields navigation
‘Star-world’ transformations
Workspace representation
No moving obstacles
Elliptical fields representation
Unpredictable control inputs
Normalized control input

## Slide 30
Navigation
Control input generation
Workspace generation
Predictive fields navigation
Research
contribution
Workspace representation
Elliptical fields representation
Normalized control input
Simulated workspace
Generate waypoints to be able to track a moving goal.
One of the first experimental demonstrations of navigation functions.
Used the iRobot Roomba and Kinect to set up experiment.
Experimental verification
Predictive fields navigation

## Slide 31
Navigation
Control input generation
Workspace generation
Predictive fields navigation
Research
contribution
Experimental verification
Person following using predictive fields
Single stationary obstacle
Generate map
Detect leader occlusion
Create predictive fields workspace
Get and act on robot control input.
Continue `exact following’ when leader is reidentified.
Single moving obstacle

## Slide 32
Indoor environment
Kinect RGB-D sensor
Pioneer P3-AT robot
Leader tracking
Kinect skeletal tracker
Appearance descriptor generation
Leader detection, occlusion inference
Mapping
Floor occupancy detection
Manhattan rotation
Local environment map generation
Translation estimation
Mobile robot person following system
Navigation
Control input generation
Workspace generation
Predictive fields navigation

## Slide 33
Research contributions
Mobile robot person following system
Person follower classification system
Occlusion detection and recovery system
Simple mapping algorithm for indoor environments
Path planning approach sensitive to obstacle motion
Method to generate practical control inputs to robot
Practical representation of robot workspaces
Experimental verification of navigation function path planning
Questions?