## Slide 1
Brian Peasley
PhD Candidate
Clemson University
Large Scale 3D Mapping of Indoor
Environments Using a Handheld RGBD Camera

## Slide 2
What is 3D Mapping?
3D Reconstruction of an environment using multiple data points from a sensor and recovery of that sensors trajectory.

## Slide 3
3D Mapping Outline
Sensor
Reading
Camera
Tracking
Integration
Model
Loop Closure
Detection
Loop
Closing
Static Scene
T

## Slide 4
Why?
Robotics:
Navigation
Object Manipulation
Computer Graphics:
Augmented Reality
Compositing
Medical:
Aid In Surgery
Monitor Prenatal Development

## Slide 5
Simple 3D Mapping System
Manhattan Constraint
All walls are parallel or perpendicular:
Mapping to Model
  Reduce Drift
  Obviate Loop Closures
Examine Multi-Resolution Hierarchical Representations
  Memory efficient
  Allows for large scale reconstructions
Sensor
Reading
Camera
Tracking
Integration
Model
Loop Closure
Detection
Loop
Closing

## Slide 6
Simple 3D Mapping System
Traditionally estimate pose w.r.t. previous sensor reading
Map to Model (errors do not compound)
Model
Sensor
Reading
Camera
Tracking
Integration
Model

## Slide 7
Simple 3D Mapping System
Robot Pose
Visual
Odometry
Onboard
Odometry
Manhattan
Constraint
B. Peasley, S. Birchfield, A. Cunningham, and F. Dellaert. “Accurate on-line 3D occupancy grids using Manhattan world constraints”, International Conference on Intelligent Robots and Systems (IROS), 2012.
Model
All walls are parallel or perpendicular
Sensor
Reading
Camera
Tracking
Integration
Model

## Slide 8
Simple 3D Mapping System

## Slide 9
Simple 3D Mapping System

## Slide 10
Simple 3D Mapping System
Sensor
Reading
Camera
Tracking
Integration
Model
53m x 53m x 4m
(30 mm resolution)
7,789 RGBD Images
@ 640x480
Point Clouds:
  # 3D Points = 7,789 x (640 x 480)
  1 Colorless 3D Point = 12 Bytes
  1 Colored 3D Point = 15 Bytes
  Reconstruction Memory Usage:
  Colorless ~ 28.71 GB
  Colored ~ 35.89 GB

## Slide 11
Simple 3D Mapping System
53m x 53m x 4m
(30 mm resolution)
7,789 RGBD Images
@ 640x480
3D Occupancy Grid
Save reconstruction in a voxel volume.
3D binary image
Each voxel is occupied or free
More voxels = higher resolution
To store as colored 3D occupancy Grid:

## Slide 12
Simple 3D Mapping System
Octrees
Hierarchical Representation
Only allocates memory needed
Requires ~2.6 bits to store a voxel
Illustrated with Quadtrees and pixels
M. Botsch, A. Wiratanaya, and L. Kobbelt. Efficient High Quality Rendering of Point Sampled Geometry. In Thirteenth Eurographics Workshop on Rendering, 2002.

## Slide 13
Simple 3D Mapping System
53m x 53m x 4m
(30 mm resolution)
7,789 RGBD Images
@ 640x480
50m x 24m x 5m
(30 mm resolution)
3,300 RGBD Images
@ 640x480
Colorless:
Point Cloud: 12.7 GB
Occ. Grid (30 mm): 22.2 MB
Occ. Grid (4 mm): 93.75 GB
Octree (30mm): 941 KB
Colorless:
Point Cloud: 28.7 GB
Occ. Grid (30 mm): 41.6 MB
Occ. Grid (4mm): 175.56 GB
Octree (30mm): 5.6 MB

## Slide 14
Simple 3D Mapping System
Sensor
Reading
Camera
Tracking
Integration
Model
What did we learn?
Mapping to model:
Useful for reducing drift
World isn’t always as simple as a Manhattan World
Multi-Resolution Representation:
Greatly reduces the amount of memory required to store a reconstruction

## Slide 15
Kinect Fusion
Sensor
Reading
Camera
Tracking
Integration
Model
R. A. Newcombe, S. Izadi, O. Hilliges, D. Molyneaux, D. Dim, A. J. Davison, P. Kohli, J. Shotton, S. Hodges, and A. Fitzgibbon. KinectFusion: Real-time Dense Surface Mapping and Tracking. In Proceedings of the 10th IEEE International Symposium on Mixed and Augmented Reality (ISMAR), pages 127-126, 2011.

## Slide 16
Kinect Fusion
Truncated Signed Distance Function (TSDF)
3D Voxel Volume
Each voxel contains signed distance to nearest surface
Distances bounded by an upper limit (truncated)
positive = inside an object
negative = outside an object

## Slide 17
Kinect Fusion
Last estimated pose
Reconstructed Scene
Surface
Estimation
Current
Frame
Sensor
Reading
Camera
Tracking
Integration
Model

## Slide 18
Kinect Fusion
Limitations
  Environment Size
    Reconstruction is bounded to a TSDF volume
    TSDF memory consumption exponentially increases with size and resolution
  Camera Tracking
    Only uses depth, fails when little geometry is present
    Cannot maintain tracking with sparse depth information
TSDF
TSDF

## Slide 19
Camera Tracking
Iterative Closest Point (ICP)
Correspondence
Weighting
Rejection
Error Metric
Minimize
Update
Family of algorithms that iteratively aligns two point clouds together in a 6 step process.
Given two point clouds, find all matching points.

## Slide 20
Compute q0
q1
q0
q2
q3
Camera Tracking
Projective Data Association (PDA)
P
DQ
Q
p1
p2
p3
p0
Project p0 onto DQ
G. Blais and M. Levine. “Registering multiview range data to create 3D computer objects”, IEEE Transactions on Pattern Analysis and Machine Intelligence (PAMI), 1995.

## Slide 21
Camera Tracking
Overcoming Limitations of PDA
Limitations:
Fails in areas with few salient geometric features (flat walls, long hallways)
Clouds must be initially relatively close
Greatly affected by noisy or sparse depth data.
Lucas-Kanade Data Association (LKDA)
Maintains tracking in geometrical featureless environments
Clouds to not need to be closely aligned
Maintains tracking with sparse depth information
Correspondences only computed once

## Slide 22
Camera Tracking
Lucas-Kanade
I
J
Iteratively align two images:
Linearize about current estimate and solve a standard linear system.

## Slide 23
Camera Tracking
Lucas-Kanade Data Association (LKDA)
Q
P
DQ
DP
CP
CQ
Project pi onto CP
pi
qi
Map to DQ
B. Peasley and S. Birchfield, “Replacing Projective Data Association with Lucas-Kanade for KinectFusion”, International Conference on Robotics and Automation, 2013.

## Slide 24
Camera Tracking
Iterative Closest Point (ICP)
Correspondence
Weighting
Rejection
Error Metric
Minimize
Update
Projective Data Association
Lucas-Kanade Data Association
LKDA
Sum of Squared distances between corresponding points “point-to-point”
Sum of squared distances from each source point to the plane containing the destination point “point-to-plane”

## Slide 25
Camera Tracking
Point-to-Plane Error Metric and Minimization
Error Metric:
q1
q0
q2
q3
p1
p2
p3
p0
n0
n1
n2
n
Iterative minimization: T contains non-linear components. Linearize about current estimation and solve linear system.

## Slide 26
Camera Tracking
Point-to-Plane Limitation

## Slide 27
Camera Tracking
Point-to-Point Error Metric and Minimization
q1
q0
q2
q3
p1
p2
p3
p0
Error Metric:
Minimization:
Iterative: Linearize about current estimation and solve linear system.
Direct: Procuste’s Analysis (sensitive too noise)

## Slide 28
 | Convergence Speed | Alignment Accuracy | Direct Solution
Point-to-Plane |  |  | 
Point-to-Point |  |  | 
*limited by geometry
Camera Tracking
Choosing Error Metric
 | Low Geometry | High Geometry
Point-to-Plane |  | 
Point-to-Point |  | 
Correspondence Accuracy inversely proportional to “amount of geometry”
(condition number of C)

## Slide 29
Camera Tracking
Error vs Condition Number
Low Geometry High Geometry

## Slide 30
Camera Tracking
Cumulative Errors
Low Geometry High Geometry

## Slide 31
Camera Tracking
Iterative Closest Point (ICP)
Correspondence
Weighting
Rejection
Error Metric
Minimize
Update
LKDA
k = Number of iterations

## Slide 32
Camera Tracking
Outside Bounds of TSDF
PDA
LKDA
Frame #

## Slide 33
Camera Tracking
Outside Bounds of TSDF
PDA
LKDA

## Slide 34
Camera Tracking
Flat Wall
PDA
LKDA
Frame #

## Slide 35
Camera Tracking
Flat Wall
PDA
LKDA

## Slide 36
Camera Tracking

## Slide 37
Camera Tracking

## Slide 38
Kinect Fusion
Limitations
  Environment Size
    Reconstruction is bounded to a TSDF volume
    TSDF memory consumption exponentially increases with size and resolution
  Camera Tracking
    Only uses depth, fails when little geometry is present
    Cannot maintain tracking with sparse depth information
TSDF
TSDF

## Slide 39
TSDF vs. Occupancy Grid
TSDF
Occupancy Grid

## Slide 40
TSDF vs. Occupancy Grid
TSDF (4 Bytes per cell)
Occupancy Grid (1 byte per cell)
Negative
Positive
Occupied
Free

## Slide 41
TSDF vs. Occupancy Grid
TSDF
Occupancy Grid
0
0

## Slide 42
TSDF vs. Occupancy Grid

## Slide 43
TSDF vs. Occupancy Grid
 | TSDF | Occ. Grid
Memory | Typically 4 bytes per cell | Typically 1 byte per cell (Can use 1 bit)
Continuous | Each 3D point can be interpolated to obtain distance to nearest surface | Each 3D point is classified as occupied or unoccupied
Noisy Data | Update step smooths surface | Techniques do exist to smooth surface, take a long time (MCMC). Memory goes up to 4 bytes per cell
Updating | More complex | Simple

## Slide 44
TSDF vs. Occupancy Grid

## Slide 45
TSDF vs. Occupancy Grid

## Slide 46
TSDF vs. Occupancy Grid

## Slide 47
Loop Closing
Sensor
Reading
Camera
Tracking
Integration
Model
Loop Closure
Detection
Loop
Closing

## Slide 48
Estimated Trajectory
Same Point
Close Loop
Loop Closing

## Slide 49
Loop Closing
Graph Optimization
State
Measurement
(typically relative)
Actual
Observation
Predicted
Observation
Minimize

## Slide 50
Loop Closing
Minimize
Nonlinear
Solved Incrementally
“A little bit of math shows…”
Jacobian of the error (negative of residual)
w.r.t. the state
Increment to the state space
Residuals stacked vertically
Linearized
State Space
K = Variances concatenated horizontally

## Slide 51
Loop Closing
Iterative Techniques
 | Edges | Easily Trapped | Fast Convergence | Expensive
Newton-Rapshon | All | yes | yes | yes
Gradient Descent | All | yes | yes | yes
Conjugate Gradient Descent | All | yes | yes | yes
Simplex Methods | All | yes | yes | yes
Gauss-Seidel | All | yes | If near solution | no
Stochastic Gradient Descent | Single | no | no | no

## Slide 52
Loop Closing
State Space
Global State Space (x, y, θ)

## Slide 53
Loop Closing
State Space
Incremental State Space (Δx, Δ y, Δ θ)
Edwin Olson, J. Leonard, and S. Teller. Fast Iterative Optimization of Pose Graphs With Poor Initial Estimates. In Proceedings of the International Conference on Robotics and Automations (ICRA), pages 2262-2269, May 2006.

## Slide 54
Loop Closing
State Space
Relative State Space (Δx, Δ y, Δ θ)

## Slide 55
Loop Closing
Proposed Approach
Two Phase System
Stochastic Gradient Descent with Relative State Space (POReSS)
  RSS allows multiple poses to be effected in each iteration
  SGD prevents from being trapped in local minima
  Result: Quickly gets to a “good” solution
  Drawback: Long time to convergence
Gauss-Seidel with Global State Space (Graph-Seidel)
  Seed with output from POReSS
  GSS only changes one pose at a time in each iteration
  Gauss-Seidel allows for quick calculations
  Result: Fast “fine tuning”

## Slide 56
Loop Closing
Phase 1 Pose Optimization using a Relative State Space (POReSS)
Only Consider One Edge (SGD)
)
Precomputed
Computation of
ISS
a+1 b
RSS
Between Consecutive nodes

## Slide 57
Loop Closing
Pose Optimization using a Relative State Space (POReSS)

## Slide 58
Loop Closing
Phase Two Gauss-Seidel using Global State Space (Graph-Seidel)
Gauss-Seidel is a method for solving the standard linear system
(nonlinear)
Ab
Evaluate at current estimate
Avoid explicitly calculating A and b, especially for large graphs. (Graph-Seidel)
(GSS)

## Slide 59
Loop Closing
Phase Two Gauss-Seidel using Global State Space (Graph-Seidel)
A
x
b
A
Diagonal: Function of connected nodes diag()
Everything else: Connectivity ( if connected, 0 otherwise)
b
Sum of edges in – sum of edges out
constant

## Slide 60
Loop Closing
Phase Two Gauss-Seidel using Global State Space (Graph-Seidel)
A (constant)
Diagonal: Function of connected nodes diag(())
Everything else: Connectivity ( if connected, 0 otherwise)
b
Sum of edges in – sum of edges out

## Slide 61
Loop Closing
Phase Two Gauss-Seidel using Global State Space (Graph-Seidel)
Form linear system
Compute new state
Using Graph-Seidel

## Slide 62
Loop Closing
Phase Two Gauss-Seidel using Global State Space (Graph-Seidel)

## Slide 63
Loop Closing
POReSS + Graph-Seidel

## Slide 64
Loop Closing
POReSS + Graph-Seidel

## Slide 65
Loop Closing
POReSS + Graph-Seidel

## Slide 66
Loop Closing
rPOReSS
Majority of drift is caused by rotational errors
Remove rotational drift
Treat (x,y) components of poses as constants.
Greatly reduces complexity of Jacobian derivation
1xN

## Slide 67
Loop Closing
rPOReSS

## Slide 68
Loop Closing
rPOReSS

## Slide 69
Loop Closing
irPOReSS
Incremental:
Rotational POReSS can be run incrementally
Goal is to keep graph “close” to optimized
Run Graph-Seidel whenever a fully optimized graph is desired.
Further iterations of POReSS will undo fine adjustments made by Graph-Seidel.

## Slide 70
Loop Closing
irPOReSS

## Slide 71
Loop Closing
irPOReSS

## Slide 72
Conclusion
Sensor
Reading
Camera
Tracking
Integration
Model
Loop Closure
Detection
Loop
Closing
Simple Mapping System
  Demonstrated power of mapping to model
  Show capability of hierarchical multi-resolution volumes
Camera Tracking
  Used color information to drive alignment of geometric data (LKDA)
  Automatic selection of error metric
Integration
  Examined several ways to represent the reconstruction.
  Demonstrated the capabilities of the TSDF
Loop Closing
  Proposed a two phase system of graph optimization
  Proposed a method for graph optimization using a RSS
  Proposed a version of Gauss-Seidel optimized for graphs.

## Slide 73
Questions?